## Slide 1
CalNex Data Workshop
11-Jan-2011
Characterizing near-shore and off-shore air masses in southern CA during CalNex
Brian Lerner1, 2, Jim Johnson3, 4, Eric Williams1, 2
1NOAA ESRL CSD, Boulder CO
2CIRES, University of Colorado at Boulder
3NOAA PMEL, Seattle WA
4JISAO, University of Washington

## Slide 2
Outline
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air
Review of measurements; status of data
  “Cleaning” the data of influence from Atlantis
Gridding the data by location
Characterizing near-shore / off-shore air
  CO, NOy and O3
  Wind direction
Photochemical age
  Clean marine vs. Los Angeles bight

## Slide 3
1-min resolution files
  Gas-phase species: NO, NO2, NOy, O3, CO, CO2, SO2, H2O
  Directly measured photolysis rates: NO2, NO3, O3→O[1D]
  Derived photolysis rates: ClNO2, Cl2, HONO, HCHO, etc.
  Met. data: T, RH, pressure, wind speed and direction
    1-s resolution data available by request
Overview of measurements
“Final” data has been posted on the data server:
  http://www.esrl.noaa.gov/csd/tropchem/2010calnex/
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air

## Slide 4
Sampling
Main inlet and anemometer located at starboard, forward corner of walk-up tower.
Due to location of tower relative to Atlantis exhaust stack, data filtered by relative wind direction from stern [135° wedge] and relative wind speed [< 0.02 m/s].
This removes ≈ 4.4% of sampling time from the dataset.
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air

## Slide 5: Working with the data
Traditionally, we work with data using time series
How about another approach?
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air

## Slide 6: Working with the data
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air
Putting the data on a map
Notes: Introduce the grid on CA overview map
Show grid as a fxn of:
  Time in grid
  Time of day (6 steps)
  Wind direction (6 steps)
  Chemical species: CO and NOx
Using the grid
  Aggregating the data when appropriate
  Identifying key sample locations
    Ports
    Airport
    Coastal LA
    Santa Cruz
    Carquinez Strait/Sacramento

## Slide 7: Emissions and photochemistry by location
Comparison of CO and O3 footprint
CO gradient decreases as ship moves away from the coast
Ozone gradient increases as ship moves away from the coast
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air

## Slide 8
Observable gradient from coast out to sea:
  What about NOx?
  NO primarily emitted, but significant NO2 measured.
  Rapid titration reaction with ozone
    NO + O3 → NO2 + O2
  Better to consider Ox [= NO2 + O3]
Emissions and photochemistry by location
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air

## Slide 9
How do the species mixing ratios change as a function of wind direction?
Emissions and photochemistry by location
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air
Notes: Watching the mix change as a function of wind direction
Why do highest Ox mixing ratios coincide with S and SW flow?
How does time of day correlate with wind direction?
Dividing the grid into regions: Inshore/offshore LA basin (LA and Orange Counties)
Two grid cells removed from grouping: LAX and ports (special cases)

## Slide 10
Dividing the grid into regions: near-shore/off-shore LA basin (LA and Orange Counties)
Two grid cells removed from grouping: LAX and ports (special cases)
Aggregating the data by location
Near
Off
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air
CO
CO
NOx & NOy
NOx & NOy
O3 & Ox
O3 & Ox

## Slide 11
A further look at off-shore air
Ox vs. CO
How can we make sense of this scatterplot?
With a digression . . .
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air

## Slide 12: Characterizing marine background
NOx < 0.25 ppbv
Radon < 200
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air
Trend likely from mixing of clean tropical and very old polluted air

## Slide 13
A further look at off-shore air
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air
How does the SB-Monterrey air compare with So. CA off-shore air?
Finding a correlation in the off-shore data:
  What is reasonable?
Increasing slope = more processing

## Slide 14: What’s next to do?
How well does Flexpart predict CO, NOy, etc. at ship location?
Can we characterize the source and age of the ozone-enriched air off-shore?
How does air transported across LA basin to Pasadena compare to air that ages over the water?
Summary
Evaluating dataset by location important to making sense of observations
Near-shore air shows marked differences in photochemical processing as a function of wind direction
Off-shore air generally well-mixed, independent of wind direction
  OVOCs? Organic acids? SOA?
CalNex data workshop: Outline / Data overview / Working with the data / So. CA: CO, NOx and O3 / Marine air / Characterizing LA bight air