## Slide 1: Comprehensive Isotopic Composition of Atmospheric Nitrate during CalNex
Inferring Sinks and Sources of NOX from Nitrate Stable Isotope Ratios
William C. Vicars, Samuel Morin, and Joël Savarino
Laboratoire de Glaciologie et Géophysique de l’Environnement Université Joseph Fourier, CNRS, Grenoble, France

## Slide 2: Stable Isotope Basics
Oxygen: 16O, 17O, 18O
Nitrogen: 14N, 15N
Atmospheric nitrate (HNO3 / NO3-) isotope ratios (17O/16O, 18O/16O, and 15N/14N) serve as interpretive tools to quantify NOX sources and removal mechanisms
Delta (δ and Δ) values in units of “per mil” (‰)
δ17Osample = (17O/16O)sample / (17O/16O)standard - 1

## Slide 3: Stable Isotope Basics
Oxygen: 16O, 17O, 18O
Nitrogen: 14N, 15N
Atmospheric nitrate (HNO3 / NO3-) isotope ratios (17O/16O, 18O/16O, and 15N/14N) serve as interpretive tools to quantify NOX sources and removal mechanisms
Delta (δ and Δ) values in units of “per mil” (‰)
δ18Osample = (18O/16O)sample / (18O/16O)standard - 1

## Slide 4: Stable Isotope Basics
Oxygen: 16O, 17O, 18O
Nitrogen: 14N, 15N
Atmospheric nitrate (HNO3 / NO3-) isotope ratios (17O/16O, 18O/16O, and 15N/14N) serve as interpretive tools to quantify NOX sources and removal mechanisms
Delta (δ and Δ) values in units of “per mil” (‰)
δ15Nsample = (15N/14N)sample / (15N/14N)standard - 1

## Slide 5: Stable Isotope Basics
Oxygen: 16O, 17O, 18O
Nitrogen: 14N, 15N
Atmospheric nitrate (HNO3 / NO3-) isotope ratios (17O/16O, 18O/16O, and 15N/14N) serve as interpretive tools to quantify NOX sources and removal mechanisms
Delta (δ and Δ) values in units of “per mil” (‰)
Δ17O = δ17O - 0.52*δ18O

## Slide 6: The Oxygen Isotope “Anomaly” (Δ17O) of Ozone
Thiemens, 2006, Annu. Rev. Earth Planet Sci.
O3 tropo.
δ17O = 0.52*δ18O
Δ17O = 0
Δ17O = 20-35 ‰

## Slide 7: Isotope Transfer During NOX Oxidation
NO
O3
X
XO
NO2
RO2
XO
XONO2
NO3
N2O5
O3
NO2
RH
OH
Nighttime
Daytime
HNO3
Lower Δ17O Transfer
Higher Δ17O Transfer
time scale: minutes
hours to days
heterogeneous

## Slide 8: Δ17O of Atmospheric Nitrate as a Useful Tool in Atmospheric Chemistry
Morin et al., 2008, Science
Seasonal minimum values concurrent with low O3 (polar day, daytime chemistry)
Δ17O (NO3-) values higher in winter due to increased interaction with O3 (polar night)
Seasonal maxima reflect interaction of NOx with BrO and are not predicted by O3 chemistry alone

## Slide 9: CalNex 2010
High Volume PM sampling
63 sets of samples
  coarse and fine fractions (1 μm cut-point)
26 sets from S. Cal. are 12 hour (day and night) collections (May 15 - 28)
  daytime vs. nighttime chemistry
34 subsequent sets have lower sampling durations (May 29 - June 7)
LA
San Francisco
San Diego

## Slide 10: Atmospheric Nitrate Concentration During CalNex
LA
San Francisco
San
Diego
 | Ave. | Max. | Min. | Std. Dev.
LA | 2348 | 5475 | 409 | 1382
SF | 419 | 857 | 178 | 191

## Slide 11: Air Mass Origins during CalNex

## Slide 12: O3 and NOX during CalNex
O3
NO
NO2

## Slide 13: Particle Size Distribution of Nitrate
LA
San Francisco
San
Diego
 | Ave. | Max. | Min. | Std. Dev.
LA-C | 1861 | 5101 | 330 | 1153
LA-F | 487 | 2808 | 79 | 512
SF-C | 224 | 392 | 87 | 97
SF-F | 195 | 481 | 42 | 138

## Slide 14: Oxygen Isotope Anomaly (Δ17O) of Atmospheric Nitrate
LA
San Francisco
San
Diego
 | Ave. | Max. | Min. | Std. Dev.
LA | 25.3 | 29.2 | 21.9 | 1.6
SF | 21.8 | 23.0 | 20.5 | 1.2

## Slide 15: Δ17O (NO3-) - Diurnal Variations

## Slide 16: Δ17O (NO3-) - Diurnal Variations

## Slide 17: Lifetime Effect of Atmospheric Nitrate
Typical atmospheric residence time (τ) of 1 day
  Function of NO3- particle size distribution (i.e., deposition velocity)
CalNex May 15-28 samples were collected from approx. 9am - 7pm (“day”) and 7pm - 9am (“night”)
  Mixing of “daytime” and “nighttime” Δ17O signal
Morin et al., 2010, EGU Annual Meeting

## Slide 18: Δ17O (NO3-) - Diurnal Variations

## Slide 19: Δ17O (NO3-) - Diurnal Variations

## Slide 20: Pn and Pd
A simplified Δ17O (NO3-) interpretive framework
Based on isotope mass balance, Δ17O (NO3-) is expected to be proportional to the the ratio of nighttime to daytime nitrate production
Pn
NO2 + O3  NO3 + O2
Pn α k [NO2] [O3]
Pd
NO2 + OH  HNO3
Pd α k [NO2] [OH]
Δ17O (NO3-) α Pn/(Pn + Pd)
j(O3)

## Slide 21: Pn / (Pn + Pd) and Δ17O (NO3-) Co-evolve

## Slide 22: Pn / (Pn + Pd) and Δ17O (NO3-) Co-evolve

## Slide 23: Towards a Better Understanding of the CalNex Δ17O (NO3-) Data
P1
P2
P3
NO2 + OH + M  HNO3 + M
NO2 + O3  NO3 + O2 and NO3 + RH (DMS)  HNO3 + products
NO2 + NO3  N2O5 and N2O5 + H2O(surface)  2HNO3(aq)
Michalski et al., 2003, Geophys. Res. Lett.
Air Mass Chemical Histories
3 days preceding sample collection along air-mass trajectory
NO3- concentration and residence time (split into size fractions)
NO, NO2, NO3, N2O5, O3, HO2, OH, H2O2
T and P
Relative Humidity
Agreement between modeled and measured Δ17O

## Slide 24: δ15N and NOX Source Apportionment
δ15N of atmospheric NO3 can help elucidate sources of NOX to the atmosphere, but the data is often difficult to interpret
  fuel combustion: 6-13 ‰
  soil (biological): < -20 ‰
  lightning: ≈ 0 ‰
Differences in δ15N between coarse and fine particles may be useful diagnostic tools
δ15Nsample = (15N/14N)sample / (15N/14N)standard - 1

## Slide 25: δ15N of Atmospheric Nitrate
LA
San Francisco
San
Diego
 | Ave. | Max. | Min. | Std. Dev.
LA | 0.2 | 8.0 | -4.6 | 3.5
SF | -0.6 | 1.8 | -6.2 | 3.7

## Slide 26: δ15N (NO3-): Coarse vs. Fine Particles
Average Difference = 2.3 (± 1.5)
13%
Average Difference = 2.7 (± 1.8)
27%

## Slide 27: Summary
Variations in Δ17O (NO3-) during CalNex are a function of the relative importance of “daytime” (P1) and “nighttime” (P2 and P3) reaction mechanisms
  Offset in data due to residence time effect of NO3-
A more thorough interpretation of the atmospheric Δ17O (NO3-) signal will require detailed modeling of the dominant reaction mechanisms
  Potential for collaboration, joint publications, etc.

## Slide 28: Summary
Small differences in δ15N between coarse and fine particles suggest a common source of NOX in both size fractions
  Different reaction mechanisms (P1, P2, P3) leading to NO3- formation are sensitive to particle size
  Higher δ15N in S. Cal. May reflect greater contribution of NOX from fuel combustion
The higher Δ17O (NO3-) for the samples collected near Los Angeles may be due to the greater abundance of coarse particle mass
  Greater HNO3 production via N2O5 hydrolysis in coarse particles?

## Slide 29: Thank You!

## Slide 30: δ18O and δ17O
Δ17O = δ17O - 0.52*δ18O = 0
slope = 0.52
Terrestrial Fractionation Line
For most oxygen-bearing compounds:
δ17O = 0.52*δ18O

## Slide 31: The Oxygen Isotope “Anomaly” (Δ17O) of Ozone
For Ozone (O3):
δ17O ≠ 0.52*δ18O
Δ17O = δ17O - 0.52*δ18O = 20-35 ‰
Thiemens, 2006, Annu. Rev. Earth Planet Sci.

## Slide 32: Isotope Transfer During NOX Oxidation
NO2 + O3 NO3 + O2
N16O18O + 16O18O17O N16O18O17O + 16O18O
For Atmospherically-Derived Nitrate (NO3-):
Δ17O = δ17O - 0.52*δ18O =
20-30 ‰ (tropospheric O3), 30-40 ‰ (statospheric O3)
Important nighttime NO2 removal mechanism

## Slide 33: δ15N (NO3-) - Diurnal Variations